A practical guide to IP Networking
OSI Model
Layer 1 (Wires)
Layer 2 (MAC Addresses)
Layer 3 (IP addresses)
Layer 4 (IP Services)
From IPv4 to IPv6

---
A practical guide to IP Networking
There's no place like 127.0.0.1

---
OSI Model

---
OSI Model

---
Layer 1
UTP Cables
Fiber optic cables
Wireless
The bits of data!
Full-Duplex/Half Duplex

---
Layer 1
A word about UTP Cables (CAT 5/5e/6/7/etc)
„Twisted pair cabling is a type of wiring in which two conductors of a single circuit are twisted together for the purposes of canceling out electromagnetic interference“
Unshielded Twisted Pair
Shielded Twisted Pair
'Straight-through' or 'Cross'
Wiring according to: T568A/T568B

---
Layer 1
A word about UTP Cables (CAT 5/5e/6/7/etc)
„Twisted pair cabling is a type of wiring in which two conductors of a single circuit are twisted together for the purposes of canceling out electromagnetic interference“
Unshielded Twisted Pair
Shielded Twisted Pair
'Straight-through' or 'Cross'
Wiring according to: T568A/T568B

---
Layer 1
A word about UTP Cables (CAT 5/5e/6/7/etc)
„Twisted pair cabling is a type of wiring in which two conductors of a single circuit are twisted together for the purposes of canceling out electromagnetic interference“
Unshielded Twisted Pair
Shielded Twisted Pair
'Straight-through' or 'Cross'
Wiring according to: T568A/T568B

---
Layer 1
Grab a UTP cable and connect it to your laptop or computer
Start your computer with a PXE boot
Enter 'ipws' at the prompt
Once booted to the prompt disconnect your UTP cable from the switch

---
Layer 2
To Know:
MAC Address – a unique 64bit address which identiefies your NIC (Network Interface Card)
MAC first 24bit == manufacterer ID
Happens before routing! (or after)
Subnet / Broadcast domain – often used names for the layer 2 network

---
Layer 2
Login as root on your computer
Execute 'ifconfig eth0'
Find the 'Hwaddr' value of your NIC
Execute 'ethtool eth0' (check it's output)
Connect your UTP cable to your neighbour or a switch
Execute 'ethtool eth0' again (check it's output)

---
TCPdump
 „a powerful command-line packet analyzer“
„tcpdump - dump traffic on a network“
We'll use tcpdump to sniff the network in order to see what we are doing

---
TCPdump
Access the second terminal on your computer (ALT+F2)
Login as root
Execute 'tcpdump -i eth0 -ntev'
-i	interface
-n	no name resolving (DNS)
-t	no timestamp
-e	show link-level header (layer 2)
-v	extra output (verbose)
Execute 'ifconfig eth0 up' to bring your interface up
Execute 'tcpdump -i eth0 -nte'
Switch back and forth to the first (tty1) and second terminal (tty2) (ALT+F1/ALT+F2)

---
Layer 3
To Know:
IP Address – a 32bit address which identifies your computer
Subnet Mask – identifies the scope of your layer 2 network! (netmask)
ARP – resolve ipaddresses to MAC addresses
Route – a table to find your way out of the layer 2 network/subnet/broadcast domain

---
Layer 3
128 64 32 16 8 4 2 1
    1 0 0 1 0 0 0 1
128 + 16 + 1 = 145

---
Layer 3
Private IP adress ranges:
10.0.0.0/255.0.0.0 (/8)
172.16.0.0/255.240.0.0 (/12)
192.168.0.0/255.255.0.0 (/16)
169.254.0.0/255.255.0.0 (/16) used for non dhcp networks/autoconf
Special Ranges
224.0.0.0/240.0.0.0 (/4) multicast address space
127.0.0.1/255.0.0.0 (/8) loopback address space
0.0.0.0/255.0.0.0 (/8) broadcast addresses
255.255.255.255/255.255.255.255 (/32) limited broadcast
All address space is maintained by IANA

---
Layer 3
Ip address and it's subnet mask???
Imagine 192.168.1.1 with a subnet mask 255.255.255.0 (/24)
In bits
Ip:	1 1 0 0 0 0 0 0 . 1 0 1 0 1 0 0 0 . 0 0 0 0 0 0 0 1 . 0 0 0 0 0 0 0 1
Mask:	1 1 1 1 1 1 1 1 . 1 1 1 1 1 1 1 1 . 1 1 1 1 1 1 1 1 . 0 0 0 0 0 0 0 0
        8 bits + 8 bits + 8 bits + 0 bits = 24bits

---
Layer 3
Ip address and it's subnet mask???
Imagine 192.168.1.1 with a subnet mask 255.255.255.0 (/24)
In bits
Ip:	1 1 0 0 0 0 0 0 . 1 0 1 0 1 0 0 0 . 0 0 0 0 0 0 0 1 . 0 0 0 0 0 0 0 1
Mask:	1 1 1 1 1 1 1 1 . 1 1 1 1 1 1 1 1 . 1 1 1 1 1 1 1 1. 0 0 0 0 0 0 0 0
        8 bits + 8 bits + 8 bits + 0 bits = 24bits

---
Layer 3
On your computer give your NIC an ip address in the 192.168.25.0/24 subnet:
Example for a 10.11.12.0/24 subnet:
ifconfig eth0 10.11.12.100 netmask 255.255.255.0 up
Try a single ping to 192.168.25.250 in your subnet and watch the output of tcpdump
ping -c 1 192.168.25.250
-c count: Stop after sending count ECHO_REQUEST packets.

---
Layer 3
ARP, Request who-has 192.168.25.250 tell 192.168.25.176, length 28
ARP, Request who-has 192.168.25.250 tell 192.168.25.176, length 28
ARP, Request who-has 192.168.25.250 tell 192.168.25.176, length 28
ARP : Address Resolution Protocol.
Resolves ip addresses to MAC addresses

---
Layer 3
Try a single ping to a neighbour in your subnet, example for the 10.11.12.0/24 subnet:
ping -c 1 10.11.12.101
Check the output of tcpdump!!!

---
Layer 3
Check the output of tcpdump!!!
ARP, Request who-has 192.168.25.1 tell 192.168.25.176, length 28
ARP, Reply 192.168.25.1 is-at 00:0f:1f:73:ea:d6, length 46
On your computer execute:
'arp -an'
-a	display all
-n	numeric, no resolving

---
Layer 3
On your computer execute:
'ping 8.8.8.8'
Introducing routing

---
Layer 3
Remember:
When you address a host within your subnet you'll
use MAC addresses to communicate
Use ARP to resolve an IP address to a MAC address
When you address a host outside your subnet you'll
Look in the route table to find who knows how to find the host (most specific)
Use ARP to find the MAC address of the host who knows
Send your packet to that MAC address
This process continues untill the host has been reached!

---
Layer 3

---
Layer 3
IP packets have a TTL (Time To Live)
This prevents infinite loops!
Whatch the TTL attribute in the tcpdump output!

---
Layer 3
On your computer display your routing table:
'route -n'
Add the 8.8.8.8 host to the routing table
'route add -net 8.8.8.8 netmask 255.255.255.255 gateway 192.168.25.254'
Try to ping again and watch the tcpdump output
'ping -c 1 8.8.8.8'

---
Layer 3
This is all you need to know about how the internet works!!!
Remember internet and the network does not go beyond layer 3!
There are more features:
Routing protocols like BGP/OSPF so your route table is managed
Loop prevention through Spanning Tree, Link Aggregation, etc
More specifics for Wireless networks aka 802.11*
Redundancy and asynchronous routing
But let's focus on what we do on the network/internet
Layer 4

---
Layer 4
A warning:
Strict comparison between the TCP/IP model and the OSI model should be avoided. Layering in TCP/IP is not a principal design criterion and is in general considered to be harmful.
(wikipedia)

---
Layer 4
TCP/IP
As referred to very often however it's:
IP = The IPv4 protocol (protocol number 0)
ICMP = Internet Control Messaging Protocol (protocol number 1)
UDP = User Datagram Protocol (protocol number 17)
TCP = Transmission Control Protocol (protocol number 6)
There are way more, see /etc/protocols!

---
Layer 4
ICMP
It controls the connection
If something goes wrong ICMP will tell you
0	Destination network unreachable
1	Destination host unreachable
2	Destination protocol unreachable
3	Destination port unreachable
4	Fragmentation required, and DF flag set
5	Source route failed
6	Destination network unknown
7	Destination host unknown
Etc
Used by:
Routers
Ping
Traceroute

---
Layer 4
UDP
It is simple,
It is stateless
„fire and forget“
Usable for broadcast and multicast and very simple protocols
Used by:
DHCP (port 67 and 68)
DNS (port 53)
...

---
Layer 4
TCP
reliable,
ordered,
error-checked
connection oriented
„it gets the message across reliably“
Not usable for broadcast and multicast, d'uh
Used by:
SSH
HTTP
Lots more...

---
Layer 4
TCP & UDP ports
TCP and UDP have the same port system consisting of 65536 numbered ports
A program can listen on a port on your NIC!
Important port numbers:
0-1023 are reserved: (root only)
TCP:22 = SSH
TCP:23 = Telnet
TCP:25 = SMTP
UDP:53 = DNS
TCP:80 = HTTP
etc, see /etc/services
1024-65535 are unpriviliged
TCP:1194 = OpenVPN
UDP:1194 = OpenVPN
TCP:3306 = MySQL
TCP:3389 = RDP
etc, see /etc/services

---
Layer 4
On your computer create a program which listens on port 2000
Execute:
'nc -lnp 2000'
-l	listen mode
-n	numeric (no resolving)
-p	port number
Open a new terminal (console) and access your neighbours port
'nc ip.add.re.ss 2000'
Watch the tcpdump output
* Use -u for UDP mode

---
Layer 4
Important Services for your network:
DHCP: Dynamic Host Configuration Protocol
Uses UDP port 67 (request) and port 68 (reply)
Uses a handshake
Client broadcasts
DHCP server replies
Client request an ip address
DHCP server replies with an ipaddress
Client ACK the ipaddress
More options are available through DHCP
Default gateway
Extra routes
Boot server (PXE/TFTP)
Many more

---
Layer 4
Important Services for your network:
DNS: Domain Name System
Resolves names to ipaddresses so you don't need the remember every ip address
Your network needs at least 1 DNS resolver. (/etc/resolv.conf)
DNS is big but these are important to know:
Every domain has a authorative name server (NS record)
An hostname to an ip address is an A record
An alias (to an A record) is a CNAME
To find the mailserver of a domain you request an MX record
SRV records are for more complicated services (Jabber/XMMP)

---
Layer 4
On your computer add the following to /etc/resolv.conf
search ws.z25.lan
nameserver 192.168.25.1
request details on the z25.org domain:
Nameserver: 'dig z25.org NS'
Mail servers: 'dig z25.org MX'
Website: 'dig www.z25.org'
Jabber: 'dig _xmpp-server._tcp.z25.org SRV'